## Slide 1
NHSC PACS
Introduction to
PACS archived products
Roberta Paladini
(NSHC/Caltech)
&
The NHSC PACS Team
R. Paladini NHSC Archive Data Workshop – August 26th – 30th 2013 PACS Intro
With additional contributions from: Bruno Altieri & Roland Vavrek

## Slide 2
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
Outline of the Talk
Quick Instrument Overview: photometer & spectrometer
Photometer:
- What kind of data in the archive ?
- Archive Products Overview and Visualization in HIPE
Spectrometer:
- What kind of data in the archive ?
- Archive Products Overview and Visualization in HIPE
PACS Calibration
Herschel Pointing Error ( particularly affecting PACS..)
Visualization outside HIPE: example with RGB image
Documentation

## Slide 3
PACS Instrument Overview
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
PACS:
A Photodetector Array Camera & Spectrometer for Herschel
Image Credit: MESS Consortium
Image Credit: ESA and PACS Consortium
M51
Imaging bolometers Spectroscopy Ge:Ga array

## Slide 4
PACS Instrument Overview
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
Wavelengths & Resolution
Imaging Photometer
“Integral Field” (IFU) Spectrometer
(3D-spectroscopy)
Simultaneous ( same FOV) 60-85 mm or 85-130 mm and 130 – 210 mm imaging
FWHM: 5.5”, 6.7”, 11.5”
1.7’ X 3.5’ FOV with a 64 X 32 and
32 X 16 arrays
Point source detection limit: ~3mJy (5s, 1h)
Simultaneous ( same FOV) 57-105 mm (B3A, B2B) & 105-210 mm (R1) spectroscopy
FWHM from 9.4” to 13”
47” X 47” FOV re-arranged via an image slicer on two 16 X 25 arrays
l/Dl ~ 1500
Sensitivity: ~ 5 X 10-18 W/m2
(5s, 1h)

## Slide 5
PACS Photometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
PACS Photometer

## Slide 6
PACS Photometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
What kind of data in the archive ?
(from HSPOT: Herschel Observing Planning Tool)
This mode was found to be less efficient than “scan map”, so it was not recommended for Cycle 1/Cycle 2 observations
Scan Map
Point-source

## Slide 7
PACS Photometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
What kind of data in the archive ? – cont.
Scan Map
Large Galactic fields
Small fields centered on point-sources
Deep cosmological fields

## Slide 8
PACS Photometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
What kind of data in the archive ? – cont.
Parallel Mode: PACS & SPIRE
This mode is efficient for large maps, i.e. > 45 arcmin in size (PACS and SPIRE are separated by 21 arcmin on the focal plane)

## Slide 9
PACS Photometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
PACS Photometer Archived Products
Source:
is it point-like ?
High-pass filtering
MADMap
YES
NO
Good noise (cfr. 1/f) removal but extended/background emission is totally gone
Preserves background (cfr. emission on all angular scales) but noise removal can be more problematic

## Slide 10
PACS Photometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
Currently available from the HSA:
Level 0: raw data cubes
Level 1: data cubes calibrated in Jy/pixel, instrument effects removed and propagation of “flagged pixels” (cfr. masks). Astrometry (cfr. Pointing) attached
NOTE: Level 1 is the typical starting point for re-processing
Level 2: maps created by projecting high-pass filtered (HPF) data cube on a grid using pointing information
NOTE: one map per OBSID / extended emission is filtered out
Level 2.5 (AKA: extended pipeline): maps combining pairs (cfr. Scan/X-scan) of OBSIDs – Both MADMap and HPF maps
NOTE: MADMap preserves emission on all angular scales
Available from the HSA in SPG11:
Level 3: maps combining all observations of a given field from the same program – HPF and MADMap

## Slide 11
PACS Photometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
Example: Crab Nebula – OBSIDs: 1342204441/1342204442
Double click on the “obs” variable
1
2
3

## Slide 12
PACS Photometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
Level 0: raw data
You do not really need to look at these..

## Slide 13
PACS Photometer
R. Paladini NHSC Archive Data processing Workshop – August 26th – 30th 2013 PACS Intro
Level 1: calibrated frames
This is the starting point for reprocessing your data

## Slide 14
PACS Photometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
Level 2: per-scan maps

## Slide 15
PACS Photometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
Level 2.5: scan/X-scan High-Pass Filtered maps

## Slide 16
PACS Photometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
Level 2.5: scan/X-scan MADMap maps

## Slide 17
PACS Photometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
Summary of PACS photometer archived products
( see Herschel Product Definition Document)
Level 0:
HPENG: engineering
HPGENHK: housekeeping
HPPAVGB/HPPAVGR: Herschel PACS Photometer Averaged Blue/Red Data ( “Signal” in /0)
HPPDMCB/HPPDMCR: raw data (blue/red)
HPPHK: housekeeping
Level 1:
HPPAVGB/HPPAVGR: Herschel PACS Photometer Averaged Blue/Red Data ( “Signal” in /0)
Level 2:
HPPPMAPB/HPPPMAPR: Herschel PACS Photometer Phot-project Map Blue/Red
( “image”, “error”, “coverage”)
Level 2.5:
HPPPCOMB/HPPPCOMR: Herschel PACS Photometer Combined MADMap Blue/Red
( “image”, “coverage”, “error” in /correctedmap, /madmap, /naivemap)
HPPPMOSB/HPPPMOSR: Herschel PACS Photometer Phot-project Mosaic Blur/Red
( “image”, “coverage”, “error” in /photProject)

## Slide 18
PACS Photometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
PACS Photometer Data Volume
Data size in SPG 10 and onwards:
Level 1 frames: data cubes + pointing + HK
 Blue channel: 700 MB/hour (prime), 350 MB/hour (parallel)
 Red channel: 180 MB/hour (~ both prime/parallel)
credit: Bruno Altieri

## Slide 19
PACS Spectrometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
PACS Spectrometer

## Slide 20
PACS Spectrometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
What kind of data in the archive ?
Line Spectroscopy - short wavelength coverage, multiple lines: 1. chop-nod (pointed/raster); 2. un-chopped (pointed/raster)
Range Spectroscopy - broader wavelength coverage, multiple ranges: 1. chop-nod (pointed/raster); 2. un-chopped (pointed/raster)

## Slide 21
PACS Spectrometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
What kind of data in the archive ? - cont.
Both line and range observations can be chop-nod or unchop
Chop-nod
Un-chopped

## Slide 22
PACS Spectrometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
What kind of data in the archive ? – cont.
Both line and range observations can be pointed or raster
Pointed
Raster ( mapping)

## Slide 23
PACS Spectrometer
R. Paladini NHSC Archive Data Processing Workshop – August 26th – 30th 2013 PACS Intro
PACS Spectrometer Archived Products
L1 pacsCUBE
L2 rebinnedCUBE
L2 projectedCUBE
L1 pacsFrames

## Slide 24
PACS Spectrometer
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
Example: AFGL490 – OBSID: 1342191353
Double click on the “obs” variable
1
2
3

## Slide 25
PACS Spectrometer
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
Level 1: PacsCube
Spectrum Explorer Tool
(common to all Herschel instruments)

## Slide 26
PACS Spectrometer
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
Level 2: Rebinned Cube
Spectrum Explorer Tool
(common to all Herschel instruments)

## Slide 27
PACS Spectrometer
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
Level 2: Projected Cube
Spectrum Explorer Tool
(common to all Herschel instruments)

## Slide 28
PACS Spectrometer
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
Summary of PACS spectrometer archived products
( see Herschel Product Definition Document)
Level 0:
HPENG: engineering
HPGENHK: housekeeping
HPSDMCB/HPSDMCR: raw DecMec (blue/red)
HPSFITB/HPSFITR: Herschel PACS Spectrometer Fitted Blue/Red ( “Signal” in /0)
HPPHK: housekeeping
HPSRAWB/HPSRAWR: raw data (blue/red)
Level 1:
HPS3DB/HPS3DR: Herschel PACS Spectrometer 3D Spectral Cube Blue/Red
( “flux”, “wave”, “ra”, “dec” in, e.g., /0: L2 N1 B R(0 0))
HPSCALB/HPSCALR: calibration (response/dark)
HPSFITB/HPSFITR: fitted slopes
Level 2:
HPS3DPB/HPS3DPR: Herschel PACS Spectrometer 3D Projected Cube Blue/Red
( “image”, “coverage” in, e.g., /0: L2 N1 A R(0 0))
HPS3DRB/HPS3DRR: Herschel PACS Spectrometer 3D Rebinned Cube Blue/Red
( “image”, “ra”, “dec”, “stddev”, “exposure”, “wavegrid” in, e.g., /0: L2 N1 R(0 0)

## Slide 29
PACS Spectrometer
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
PACS Spectrometer Data Volume
Data size in SPG 10 and onwards:
Level 0 frames: data cubes + pointing + HK
 Blue/red channel: ~ 1.5 GB/hour

## Slide 30
PACS General
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
PACS Calibration
Photometer:
Point-source flux calibration is estimated from a set of 5 fiducial stars (primary calibrators). Additionally, a set of asteroids and planets is also used (secondary calibrators);
Based on this set of calibrators, the point-source flux calibration error is ~5% in all bands, with 1-2% reproducibility;
Spectrometer:
Flux calibration is estimated from a set of ~30 absolute flux sky calibrators (fiducial stars, asteroids and planets);
Based in this set of calibrators (and using the 3X3 calibration block scheme), the flux calibration error is ~7% in all bands, with 3-4% reproducibility
http://herschel.esac.esa.int/twiki/bin/view/Public/PacsCalibrationWeb

## Slide 31
PACS General
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
Herschel Pointing Error
Herschel APE History
Absolute Pointing Error (APE): this has been continuously improving over the mission. It is now of the order of 0.8”. The Herschel archive data are currently being processed with this updated APE.
Spatial Relative Pointing Error (SRPE, or relative pointing accuracy):
only measured for small raster maps; it
is of the order of 1.02”
Relative Pointing Error (RPE, or pointing stability over ~ 1 minute periods): the PACS Instrument Team is currently working on a refined pointing scheme which will allow us to reach an RPE ~ 0.3”
http://herschel.esac.esa.int/twiki/bin/view/Public/SummaryPointing
The spacecraft attitude is controlled by the Star Tracker (STR) and the gyroscopes (GYR). The STR provides the absolute reference but with limited accuracy, while GYRs are accurate but only on short timescales. In normal operations, the GYRs attitude is calibrated using the information from the STR (“filtered attitude”).

## Slide 32
PACS Products: Visualization outside HIPE
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
Question:
I am writing e.g. an ALMA proposal and want to generate a RGB image using archival Herschel data. I do not want/do not have time for HIPE.
What shall I do ??
NOTE: visualization of products is relatively simple for photometer data, not so much for spectrometer data.

## Slide 33
PACS Products: Visualization outside HIPE
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
Observation Summary: 2 cross-scan observations in PACS scan-map mode. Each scan
observation is contained in an OBSID, i.e. 1342249134 and 1342249135.
download the tarball from the HSA: rpaladin171072676.tar
“extract” the Level 2.5 map (need to unzip the .fits file):
 rpaladin171072676/1342249134/level2_5/HPPPCOMB/correctedmap/hpacs_25HPPMADB_156.08_m57.75_v1.0_17900737138902856.fits
(blue  70, MADMap, corrected map)
 rpaladin171072676/1342249134/level2_5/HPPPCOMR/correctedmap/hpacs_25HPPMADR_156.08_m57.75_v1.0_17900744102158856.fits
(red, MADMap, corrected map)
Example: RCW 49 – 70 mm & 160 mm
NOTE: RCW 49 is an extended source, so I want to use the MADMap archived products, rather than the photProject ones.

## Slide 34
PACS Products: Visualization outside HIPE
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
RCW 49 has also ancillary SPIRE observations @ 250, 350 and 500 mm
The SPIRE observations are also 2 cross-scans, in OBSIDs 1342247254 & 1342247255.
We extract the 250 mm observation:
 rpaladin171072676/1342247254/level2_5/PSW/hspirepsw_25pmp_1024_m5746_19642974044400856.fits
… and now we build our 3-color
image in ds9:
RED: SPIRE 250 mm
GREEN: PACS 160 mm
BLUE: PACS 70 mm

## Slide 35
PACS Products: Visualization outside HIPE
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
… we could have created a 3-color image in HIPE
Use HIPE task:
createRgbImage

## Slide 36
PACS Documentation
(updated in June – July ‘13)
PACS Documentation
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
Herschel Product Definition Document
http://herschel.esac.esa.int/hcss-doc-11.0/print/pdd/pdd.pdf
PACS Observer’s Manual
http://herschel.esac.esa.int/Docs/PACS/pdf/pacs_om.pdf
PACS Data Reduction Guide: Photometer
http://127.0.0.1:8082/print/pacs_phot/pacs_phot.pdf#pacs_phot
PACS Data Reduction Guide: Spectrometer
http://127.0.0.1:8082/print/pacs_spec/pacs_spec.pdf#pacs_spec
PACS User’s Reference Manual (Section 4.1.- PACS Observation Products):
http://127.0.0.1:8082/print/pacs_urm/pacs_urm.pdf#pacs_urm

## Slide 37
PACS @ NHSC
PACS Documentation
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
Roberta Paladini (Lead)
Babar Ali (calibration scientist, photometer)
Dario Fadda (calibration scientist, spectrometer)
Jeff Jacobsen (developer, spectrometer)
Cate Liu (developer, photometer)
Steve Lord (calibration scientist, spectrometer)
Yi Mei (system engineer, photometer & spectrometer)
http://nhsc.ipac.caltech.edu/helpdesk/index.php
For any questions and help with your PACS data, contact the NHSC Help Desk:

## Slide 38
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
Thank you !

## Slide 39
PACS General
R. Paladini NHSC Data Workshop – August 26th – 30th 2013 PACS Intro
How do I check the status of
the pointing products for my data ?
HIPE> obs = getObservation(1342204441, useHsa=True)
HIPE> print obs.auxiliary.pointing.version
HIPE> 2.0
HIPE > print obs.auxiliary.pointing.versionNotes
HIPE> PointingProduct with focal length correction and uncorrected filtered quaternion